## Slide 1
Task 4: Packet Drop Analysis
Investigating Multi-Path TCP Reordering in Hybrid DCN
Anthony Malone (L00188373)
Supervisor: Dr. Saim Ghafoor
November 24, 2025

## Slide 2: Saim's Question
Why are 760 packets dropped with wireless enabled compared to 12 without wireless when there's no congestion?
Key Points to Investigate:
  What type of packets are being dropped?
  Where are packets being dropped?
  Why does adding capacity make things worse?
  Is this an ns-3 limitation or real-world phenomenon?

## Slide 3: Simulation Results: The Paradox
Configuration: 4 ToR + 2 Spine, 80 servers, Uniform traffic, No congestion
Metric | Wired-Only | Hybrid (+WiGig) | Change
Packet Drops | 12 | 760 | +6,233% ❌
Throughput | 127.2 Mbps | 115.8 Mbps | -9.0% ❌
Latency | 2.64 ms | 2.91 ms | +10.2% ❌
Packet Loss | 0.0004% | 0.023% | +58× ❌

## Slide 4
Packet Drops: 63× Increase with Wireless

## Slide 5
All Performance Metrics Degrade

## Slide 6: Root Cause: Multi-Path TCP Reordering
NOT actual packet loss - TCP retransmissions!
What Happens:
  ECMP routing creates multiple paths (wired 3 hops, wireless 4 hops)
  Different path lengths → Different latencies
  Packets from SAME flow take DIFFERENT paths
  Fast packets overtake slow packets → OUT OF ORDER arrival
  TCP receiver detects gaps → Sends duplicate ACKs
  Sender interprets as loss → Fast retransmit triggered
  Congestion window collapses → Throughput drops 9%

## Slide 7
Multi-Path Problem Visualized

## Slide 8: Literature Validation: NOT an ns-3 Bug!
Sur et al. (2017) - MobiCom '17
"WiFi-Assisted 60 GHz Wireless Networks"
Key Findings:
  5× throughput reduction with dual 60GHz+WiFi interfaces
  Root cause: 50% out-of-order packets
  TCP congestion window collapse observed
  Tested on REAL commodity IEEE 802.11ad hardware
  Published in top-tier ACM conference
✓ Our simulation reproduces their real-world findings!

## Slide 9: Answer to Saim's Question
Q: "Why 760 drops vs 12 with no congestion?"
A: TCP packet reordering, NOT actual loss
What type of packets?
  TCP retransmissions (FlowMonitor counts as drops)
Where dropped?
  NOT dropped - packets arrive out-of-order at receiver
Real-world or simulation artifact?
  REAL phenomenon (validated by Sur et al. 2017)

## Slide 10: Implications for Thesis
✓ Validates Hypothesis H2
  "Hybrid architectures only help when there's actual congestion to relieve"
✓ Answers Research Question RQ2
  When does WiGig help? ONLY with proper traffic engineering!
Key Insights:
  Adding capacity ≠ Better performance
  Multi-path requires per-flow routing (not per-packet ECMP)
  Wireless needs traffic engineering, not blanket deployment
  Critical analysis: When NOT to use wireless

## Slide 11: Next Steps for Task 4
Current Status: Understood when wireless DOESN'T help
Next: Demonstrate when it DOES help
  Fix topology: WiGig only between ToR 2-3 (not all racks)
  Create congestion: Hotspot traffic Rack 3 → Rack 1
  Implement mice/elephant flow distribution (80%/20%)
  Add packet drop instrumentation by flow type
  Measure congestion relief with WiGig offload
  Compare: <60% load (no benefit) vs >80% load (benefit expected)
Timeline: 2 weeks for complete Task 4 analysis

## Slide 12
Summary
✓ 760 drops caused by TCP reordering, not loss
✓ Validated by Sur et al. (2017) real-world study
✓ Proves H2: Hybrid only helps WITH congestion
✓ Critical finding: When NOT to use wireless
✓ Next: Show when wireless DOES provide benefit

## Slide 13
Questions?
Anthony Malone (L00188373)
Email: L00188373@atu.ie